## Slide 1
EnOcean Alliance Members Meeting
Technical overview
Marian Hönsch / Technical Working Group
05.04.2018

## Slide 2: Agenda
Technology Explained in few slides
Organization: How the TWG Works & 2018 Programs Roadmap Focus 2018, Technology & Programs
IoT
EnOcean over IoT, Next gen EEP,
Product Database
Standard product Labels
2

## Slide 3: Focus 2018
Technical Task Groups
Remote Commissioning
Security
EnOcean IoT
Product Labeling
EEP – Communication Profiles
Ongoing Technical Programs
EEP Approval Committee
Certification Program
Strategic initiative

## Slide 4: Technology Explained in few slides
Title of presentation | Author | 18-04-05
4
Protocols:
EEP / Signal Telegram
Remote Management – ReMAN
Remote Commissioning - ReCOM
Smart Acknowledge
Security / Encryption
Next gen EEPs – Ideas
EnOcean over IP
Product definitions
Certification
EOA Labeling
Electronic Datasheet
Protocol Stack
Application
EEP
RECOM - REMAN
REMAN
Smart Acknowledge
Security
EnOcean Radio Protocol 1 & 2
868.3, 902, 928 MHz (Radio)

## Slide 5
Smart acknowledgement between the sensor and the actuator
EEP(EnOcean Equipment Profile): to know what kind of device, you’re actuating
Application Layer, gives the provision to potentially develop some applications, if we decide to use the complete protocol stack

## Slide 6
Title of presentation | Author | 18-04-05
Page 5
Technology Explained in few slides
Remote Commissioning

## Slide 7: Remote Management – REMAN
Title of presentation | Author | 18-04-05
6
Remote Management
Remote Commissioning
Remote Management (REMAN) :
the SYS_EX telegram and structure definition
Basic processes and function
Remote Commissioning (RECOM) :
Builds on REMAN
Defined new function codes for SYS_EX
Complex processes – link tables, device parameters, discovery
This is the interesting protocol
SYS_EX telegram:Telegram with a
Specific structure

## Slide 8: Remote Commissioning
- Use Cases
Set Up - During commissioning of newly installed networks
Maintenance - When modifications, by adding and removing devices and/or changing devices’ configuration parameters.
Replace - When replacing a non-operating device with a pre-commissioned, ready to install one.
Troubleshooting - When trouble shooting an operating EnOcean network.
EnOcean Technical Training| M. Hönsch | Oct 30-31, 2013

## Slide 9: Three pillars
(c) EnOcean | EnOcean at a Glance
8
EnOcean Eco System
Interoperable Remote Commissioning
teach-in manually
configured proprietary
limited device description
Device
Device
+ +
+
teach-in automatically
standardized remote configuration
full device description
Commissioning Tools
Remote Commissioning Device Certification
Remote Commissioning Specification
Cross-Device Interoperable Communication Standard
Standardized Device Features Description
Unified Product Labeling & Reference in Field

## Slide 10: Get Product Id
EnOcean Technical Training|
M. Hönsch |
Oct 30-31, 2013
Page 9
Commissioned device
1. Scan Product ID and EnOcean ID
https://www.qr-code-generator.com/

## Slide 11: Get Device Description file
EnOcean Technical Training| M. Hönsch | Oct 30-31, 2013
Page 10
1. Query Device Description File with Product ID
https:\\enocean-alliance.com\ddf\[MAN-ID]\[PRODUCT-ID]
2. Get DDF - XML

## Slide 12: Use case – Linking
2. Add switch to Link Table
3. Switch will immediately work
1. Scan the switch

## Slide 13: Use Case - Paramters
Set temperature in HVAC
Dimmer settings
Energy settings
Control panel set up
Timers in occupancy

## Slide 14
Title of presentation | Author | 18-04-05
Page 13
Technology Explained in few slides
Smart Acknowledge

## Slide 15: Smart Acknowledge
2nd (SMART ACK): Parameter Update
(e.g. display value, set-point zero, display “window open!”)
1st : Measurement Value
(e.g. temperature, humidity, set+, set-)
Introducing the EnOcean world | A. Pelka, M. Hönsch| May 22, 2012
Smart acknowledge bi-directional communication between a self-powered device and a line-powered device..LinePowered: In reference to equipment that is electrically powered by the telecommunications circuit to which it connects, thereby eliminating the need for local power.

## Slide 16: Smart ACK Principle
sd Reclaim process
Energy autarkic sensor
/ Post Master
Init telegram()
Reclaim()
Acknowledge()
Extremely short time interval
Only here the receiver is
switched on!
Introducing the EnOcean world | A. Pelka, M. Hönsch| May 22, 2012

## Slide 17
Title of presentation | Author | 18-04-05
Page 16
Technology Explained in few slides
Security

## Slide 18: Security level survey
Page 17
 | Metering Products (Sensors) | Comfort & Energy Saving Products (Controls power consuming or –generating devices) | Safety & Security Products (Protecting high value assets or human life)
Confidentiality | AES encryption | AES encryption | AES encryption
Authenticity | AES CMAC with counter | AES CMAC with counter | AES CMAC with counter
Integrity | AES CMAC | AES CMAC | AES CMAC
DoS Protection | Absence & Relay detection | Absence & Relay detection | Absence & Relay detection
© EnOcean
Telegram encryption (hide meaning) and authentication (avoid unauthorized control)
EnOcean score high in Fraunhofer (AISEC) security survey

## Slide 19: Encryption in Radio Telegrams – Data > EnOcean GmbH - © 2013
RORG | DATA | TXID | STATUS
0x31 | RORG | ENC_DATA | RLC | CMAC | TXID | STATUS
Secure
En- \ decapsulation of non-secure RORG
Non-secure

## Slide 20: VAES
> Titel der Präsentation > Autor > 05.04.2018
> EnOcean GmbH - © 2013
PUBLIC KEY
RLC
AES128
ENC
DATA
DATA_ENC
PRIVATE KEY
PUBLIC KEY
RLC
AES128
ENC
DATA_ENC
DATA
PRIVATE KEY
XOR
XOR
XOR
XOR
PUBLIC KEY is for all devices same
= 0x3410de8f1aba3eff9f5a117172eacabd

## Slide 21
Page 20
Technology Explained in few slides
EEP / Signal Telegram
enOcean Equipment Profile

## Slide 22: EEP / GP (Application Interface)
EEP
What is it
“Translation between Bytes and Meaning”
Mechanism to encode / interpret EnOcean telegrams based on a “magic number”
Foundation for functional interoperability between products
What should be done
  Number of defined EEP keeps growing, but support for new EEP is limited
  Short term item is to separate status & configuration from normal reporting
  Long term item is secure application level interoperability and next gen profiles
Page 21

## Slide 23: Signal Telegramm
Title of presentation | Author | 18-04-05
22
Extending devices EEP functionality with common features.
Energy storage at: 80 % Energy harvesting conditions are: “very good”
Trigger: last device status
Signal: device status
I can hear:
10 IDs with very good radio quality
5 IDs with average radio quality

## Slide 24
Title of presentation | Author | 18-04-05
Page 23
Technology Explained in few slides
EnOcean over IP

## Slide 25: IoT - All about connecting devices
Apple
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things
Page 24
Open Connectivity
Foundation

## Slide 26: EnOcean IP
Representation of EnOcean devices in IP – mostly EEP related REST Api, JSON Data Model
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things
Page 25
Nr. | JSON model
1 | systemInfo
 | version of Interface with EnOcean base information
2 | profile
 | EEP functionality / functions: Which information will send a specific profile or device and which states can be set?
3 | device
 | informations about known devices of the Interface
4 | telegram
 | incoming and outgoing telegrams
5 | state
 | saved states of devices

## Slide 27
https://www.enocean-alliance.org/wp-content/uploads/2017/05/EnOcean_Equipment_Profiles_EEP_v2.6.7_public.pdf
26
Basic structure of Interface response:
{
"header" : {
"status" : 200, "content" : "states",
"timestamp" : "2015-08-11T18:10:15.574+0200"
},
"states" : [ {
"deviceId" : "019604F9", "friendlyId" : "valve", "functions" : [ {
"key" : "setPointInverse", "value" : "0",
"valueKey" : "false",
"timestamp" : "2015-08-11T18:09:54.115+0200", "age" : "21459"
}, {
"key" : "valve",
"value" : "15",
"unit" : "%",
"timestamp" : "2015-08-11T18:09:54.115+0200", "age" : "21459"
} ]
} ]
}
146
{
"deviceId" : "019604F9", "friendlyId" : "valve",
"timestamp" : "2015-08-11T18:11:24.205+0200",
"direction" : "from",
"functions" : [ {
"key" : "valve",
"value" : "0",
"unit" : "%"
} ],
"telegramInfo" : { "data" : "8",
"status" : "0",
"dbm" : -45,
"rorg" : "A5"
}
}
REST route
HTTP method
/devices/states or /device/{deviceId}/stream
GET

## Slide 28
Title of presentation | Author | 18-04-05
Page 27
Technology Explained in few slides
Certification

## Slide 29: Certification
Title of presentation | Author | 18-04-05
28

## Slide 30: Certification Versions
EnOcean Alliance | Certification| Armin Pelka | 18th July.2017 |
Air Interface Certification
“Certified Platform”
Only for module & platform manufacturers.
Air Interface Certification
+ Profile Declaration
“Certified Product 2.0”
Only for legacy products.
Air Interface Certification
+ Profile Certification
+ Energy Harvesting Certification (Dec 17)
+ Radio performance Certification (Nov 17)
“Certified Product 3.0”
For all new products. Legacy products optional.

## Slide 31: Self-Certification. Low Effort. Low / No Cost.
EnOcean Alliance | Certification| Armin Pelka | 18th July.2017 |
EnOcean Alliance Certification Manager Armin Pelka
certification@enocean-alliance.org
Certified Product Database
https://www.enocean-alliance.org/ja/products/

## Slide 32
Title of presentation | Author | 18-04-05
Page 31
Technology Explained in few slides
Labeling

## Slide 33: Labeling
32
What is defined?
Label content is separated into fields (according to ANSI MH10.8.2-2010)
Label shall be machine readable too
Mandatory Fields:
Optional Fields:
Product ID
6 bytes
Manufacturer Assigned
EURID
4 bytes
Module manufacturer assigned
AES Security Key
16 bytes
Recom code
4 bytes
Manufacturer tags
…

## Slide 34: Labeling
33
What is up to the manufacturer?
Label type – NFC, QR, BAR etc.
Label properties: pixel size, coding, dimensions
Label position

## Slide 35
Page 34
Organisation
How the TWG Works

## Slide 36: Organisation
EnOcean Alliance
TWG
TTG
TTG
TTG
TWG – Technical Work group
TTG – Technical Task group

## Slide 37: Rules of the Game.. For content creation
TWG
TTG Create 6-12 Months
(exclusive access)
TWG Approve 4 weeks

## Slide 38
Title of presentation | Author | 18-04-05
Page 37
Organization
Focus 2018

## Slide 39: Focus 2018
Technical Task Groups
Remote Commissioning
Security
EnOcean IoT
Product Labeling
EEP – Communication Profiles
Ongoing Technical Programs
EEP Approval Committee
Certification Program
Strategic initiative

## Slide 40: Focus 2018
Remote Commissioning & Remote Management
Secure communication
Range Extension over repeater
Range Extension over multiple hops
Device Description File – extension promotion amongst members TTG Head:
EnOcean ViCOS

## Slide 41: Focus 2018
EEP Communication Profile
Definition of Signal Telegram and associated features
EEP v3 – new concept – long term
Simplified EEP Specification release process
Tool for profile submission and description
TTG Head:
TWG Chair

## Slide 42: Focus 2018
Security
Incorporate (bidirectional) high Security concept to existing specification
Review and extend existing features
Secure communication inside Recom
TTG Head:
EnOcean

## Slide 43: Focus 2018
Labeling
Review standard for multi-purpose protocol use
Promote standard to members
Incorporate feedback and expand
TTG Head (Specification owner): EnOcean GmbH

## Slide 44: Focus 2018
EAC – EEP Approval Committee (Program)
Ongoing meetings and review of new submissions of EEPs
ensure high quality standards
active support interoperability
EAC Program Updates - New Profile submits include:
  Test for EEP Certification
  IP Representation
Program Head:
Diehl

## Slide 45: Focus 2018
Certification program
Add Energy harvesting specification to the list of specifications
Promote Certification v2.0 & 3.0
Extend existing product database
Certification Manager: Armin Pelka

## Slide 46: Focus 2018
EnOcean IoT
Initiative to introduce new generation of devices with IoT features
Short Term goals:
  Include IP Description of additional EEPs
Mid Term goals:
  Certification 4.0 – application behavior certification
  Database of Device Description Files – electronic datasheet
  Mandatory Product labeling according to specification
  Next Generation EEPs 3.0
  Alliance approved commissioning tool Head:
Digital Concepts, ViCOS, EnOcean

## Slide 47: Next gen EEPs – Ideas
Title of presentation | Author | 18-04-05
46
EEP 3.0
  Similar to IP representation of Profiles
Few ideas
Fixed ranges & scaling for all future profiles
(endless variance caused more pain than gain)
Atomic functions (no complex hidden process)
Status reports & synchronization & acknowledges
Temperature | 10 bits | 0.1 Steps | -40°C to 60°C

## Slide 48: IoT - All about connecting devices
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things
Page 47

## Slide 49: Installers Tool
Page 48
Planning
Installation
Commissioning
Documentation
ReCOM & Installers Tool – Wireless Congress 2016 | Thomas Rieder – ViCOS GmbH | 2016-11-09
Key features:
Precise end application identification - Product label
Electronic data sheet
Device complies with certification and IoT ideas
  Atomic functionality
  All parameters can be read / write
  Status of synchronized over all user interface (display, phone, cloud)
  Application decision take outside end-devices
Remote commissioning support
Documentation: Back Up file

## Slide 50: Installers Tool – Implementation Scenario
Page 49
PRODUCT CATALOG
Manufacturer A
PRODUCT #A-1
PRODUCT #A-n
PRODUCT CATALOG
Manufacturer
Z
PRODUCT #Z-1
PRODUCT #Z-n
EnOcean Alliance
Look & Feel
One Single Tool, All Devices
Devices Interoperability
ReCOM Compliant, ReMAN Compliant
Product Manufacturers Distribution Channels
EnOcean Alliance Tool Manufacturer
Product Manufacturers Distribution Channels
Installer
Typically NO EnOcean Alliance Member!
Local language support is a MUST!
Installers Tool
Software Package EnOcean TRX Customer Support
DDF Format (standardized)
PCAT Format
EnOcean Product-ID EnOcean Standardized Label / QR-Code
Device Description File EnOcean Back-Up File (all standardized)
BACK-UP FILE

## Slide 51: Electronic Datasheet
Describes all features and aspects of the end product with given
semantics – configuration parameters
Publically available Standardized form
Page 50
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things

## Slide 52: Precise end-application identification
Requirement for perfect and seamless operation:
Precise end-application - Specific for final look & features
Page 51
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things Source: https://icondoit.files.wordpress.com/2010/04/nm_lightbulb.png
B
C
D
…
End-application reference: A

## Slide 53: Localization in field
Localization (e.g. in room) is required for remote set up
network identification (communication ID)
Page 52
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things Source: https://icondoit.files.wordpress.com/2010/04/nm_lightbulb.png
?
?
?
?
Communication ID | Product reference
X | Light
Y | Light
Z | Light
W | Light
ACTION: Localize Z
?
?
Z
?

## Slide 54: EnOcean becoming Things
Product
2. Query Electronic Datasheet
with End-application reference
XML
3. Commission Device
Product
Page 53
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things
  Scan communication ID
and application identification
  Get via air

## Slide 55: EnOcean becoming Things.
Key:
Specific end-application description
Identification in field
Remote control of features and configuration
(c) EnOcean Alliance | Wireless Congress 2015 | EnOcean becoming Things
Page 54

## Slide 56: IoT Spec – Coming up
EnOcean over IP
  First Specification that lays the groundwork for a complete IoT Spec
    Describes the communication behavior of a gateway between EnOcean Radio and IP-
World
  Doesn´t specify the behavior of devices (actuators, sensors)
  Doesn´t specify organizational rules for an End to End (Device to User Interface) usage
Why we need a IoT Spec.
  EnOcean has to reflect the changes and progresses in the IP/IoT world for the Ecosystem to
grow and prosper.
  First Paper Created: EnOcean devices becoming Things_IP Regulations V0.4
    Quick look through to get the idea…
What should be part of the IoT Spec
  EnOcean Specifications 2.0, 3.0
  EnOcean over IP Spec
  Existing Specifications need to be extended
  New Specifications have to be created.
Page 55
EnOcean over IP – EO Alliance Meeting London | Oliver Fischer| 24-26.04.2017

## Slide 57: IoT Spec –Content excerpt ...
Physical, Data, Network Layer
  Timing behaviour GW <-> Device
Timeslots in Adressing of devices (100 ms) Burst Avoidance
    GW -> Dimming with slider
    Device -> State reports blind actuator
  Remote Management/Remote Commissioning extension: ReMan/ReCom over repeater (similar: From Hub to Switch) ReCom: 2-Channel Actuator -> Which Switch for which channel ? ReCom: Integration of application logic into ReCom definition
  Addressing of devices with ADT, answer of devices with Broadcast)
Transport, Session Layer
  Existing Security
Key Exchange over the air …
  Security “Plus” or 2.0
Presentation, Application Layer
  Ack after Receive
  Ack after Execution
Page 56
EnOcean over IP – EO Alliance Meeting London | Oliver Fischer| 24-26.04.2017

## Slide 58
Title of presentation | Author | 18-04-05 Page 57
marian.honsch@enocean.com
Contact
For further information please feel free to contact us
EnOcean Alliance
2400 Camino Ramon, Suite. 375 San Ramon, CA 94583
USA
info@enocean-alliance.org www.enocean-alliance.org