## Slide 1: UPnP Technical basics:
UPnP Device Architecture (UDA)
July 2014
Universal Plug and Play
This now belongs to Open Connectivity Foundation, OCF

## Slide 2: UPnP Functionality
Protocol
Control
Description
Discover
Page 2
What steps are required
E.g. First request list of content transfer protocols then decide which one to use
What does a command do
E.g. setVolume – sets volume
between 1 and some device max Play
– set a MediaRenderer in PlayState
Which information is exchanged
E.g. List of supported functions grouped in services, function calls, events
How do devices detect each other
E.g. regular “alive” messages, Bye- bye messages

## Slide 3: UPnP Phases (overview)
0
1
2
3
4
5
Control points and devices get IP addresses using DHCP (, or AutoIP) Control point finds interesting device
Control point learns about device capabilities Control point invokes actions on device Control point listens to state changes of device
Control point interacts with a device with sequences of commands and events
2 Description
1 Discovery
0 Addressing
5 Protocol
4 Eventing
3 Control
Page 3

## Slide 4: UPnP Phases (Discovery)
2 Description
1 Discovery
0 Addressing
1 Find devices: Listen for SSDP Alive messages, or issue search
5 Protocol
4 Eventing
3 Control
Page 4
M-SEARCH * HTTP/1.1
HOST: 239.255.255.250:1900
M-SEARCH * HTTP/1.1 HOST: 239.255.255.250:1900
MAN: "ssdp:discover"
MX: seconds to delay response
ST: search target
HTTP/1.1 200 OK
CACHE-CONTROL: max-age = seconds until advertisement expires
HTTP/1.1 200 OK
CACHE-CONTROL: max-age = seconds until advertisement expires
LOCATION: URL for UPnP description for root device
ST: search target
USN: advertisement UUID
SSDP:Simple Service Discovery Protocol

## Slide 5: SSDP
SSDP ‐ IETF Draft Simple Service Discovery Protocol Based on UDP Multicast
Devices and services post Alive message at regular intervals
Usually repeated 3 times (because UDP messages might be lost)
Repeated every few seconds (e.g. 10 secs)
Determines worst case detection time of a device
Other Messages: Search, Bye‐Bye
NOTIFY * HTTP/1.1
HOST: 239.255.255.250:1900
NOTIFY * HTTP/1.1
HOST: 239.255.255.250:1900
CACHE-CONTROL: max-age = se
LOCATION: URL for UPnP descript
conds until advertisement expires
ion for root device
NT: search target
NTS: ssdp:alive
USN: advertisement UUID
Multicast address Port usually 1900
DLNA: port 1900 is mandatory
Location of device for further communication
Page 5
In UDP, we can unicast and multicast

## Slide 6: UPnP Phases (Description)
2
Use URL from SSDP message to get device description
Use URL from SSDP message or device description to get service description
Descriptions use XML to describe what services and functions a device offers
Find out which Optional functions are available
Find out what vendor specific functions are available
6
2 Description
1 Discovery
0 Addressing
5 Protocol
4 Eventing
3 Control
Page 6

## Slide 7: Devices
UPnP Device:
Not a real physical device
Representation of a logical entity
A set of functions and state
UPnP Device examples:
Media Server
Media Renderer
Internet Gateway device
Printer
No 1 to 1 mapping with real world devices/boxes
Page 7
TV:
PC:
Wireless Access point:
Media Player + Media Renderer Media Server + Printer + Scanner
Wireless Access point device + Printer device (proxy)

## Slide 8: Device Description – general info
<?xml version="1.0"?>
<root xmlns="urn:schemas-upnp-org:device-1-0">
<URLBase>base URL for all relative URLs</URLBase>
<device>
<friendlyName>short user-friendly title</friendlyName>
<manufacturer>manufacturer name</manufacturer>
<manufacturerURL>URL to manufacturer site</manufacturerURL>
<modelDescription>long user-friendly title</modelDescription>
<modelName>model name</modelName>
<modelNumber>model number</modelNumber>
<modelURL>URL to model site</modelURL>
<serialNumber>manufacturer's serial number</serialNumber>
<UDN>uuid:UUID</UDN>
<UPC>Universal Product Code</UPC>
<deviceType>urn:schemas-upnp-org:device:deviceType</deviceType>
<serviceList>
<service>
<serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType>
<serviceId>urn:upnp-org:serviceId:serviceID</serviceId>
<SCPDURL>URL to service description</SCPDURL>
<controlURL>URL for control</controlURL>
<eventSubURL>URL for eventing</eventSubURL>
</service>
Declarations for other services (if any) go here
</serviceList>
<deviceList>Description of embedded devices (if any) go here</deviceList>
<iconList>
<icon>
<mimetype>image/format</mimetype>
<width>horizontal pixels</width>
<height>vertical pixels</height>
<depth>color depth</depth>
<url>URL to icon</url>
</icon>
XML to declare other icons, if any, go here
</iconList>
<presentationURL>URL for presentation</presentationURL>
</device>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</root>
<?xml version="1.0"?>
<root xmlns="urn:schemas-upnp-org:device-1-0">
<URLBase>base URL for all relative URLs</URLBase>
<device>
<friendlyName>short user-friendly title</friendlyName>
<manufacturer>manufacturer name</manufacturer>
<manufacturerURL>URL to manufacturer site</manufacturerURL>
<modelDescription>long user-friendly title</modelDescription>
<modelName>model name</modelName>
<modelNumber>model number</modelNumber>
<modelURL>URL to model site</modelURL>
<serialNumber>manufacturer's serial number</serialNumber>
<UDN>uuid:UUID</UDN>
<UPC>Universal Product Code</UPC>
<deviceType>urn:schemas-upnp-org:device:deviceType</deviceType>
<serviceList>
<service>
<serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType>
<serviceId>urn:upnp-org:serviceId:serviceID</serviceId>
<SCPDURL>URL to service description</SCPDURL>
<controlURL>URL for control</controlURL>
<eventSubURL>URL for eventing</eventSubURL>
</service>
Declarations for other services (if any) go here
</serviceList>
<deviceList>Description of embedded devices (if any) go here</deviceList>
<iconList>
<icon>
<mimetype>image/format</mimetype>
<width>horizontal pixels</width>
<height>vertical pixels</height>
<depth>color depth</depth>
<url>URL to icon</url>
</icon>
XML to declare other icons, if any, go here
</iconList>
<presentationURL>URL for presentation</presentationURL>
</device>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</root>
Page 8

## Slide 9: Device Description – service information
<?xml version="1.0"?>
<root xmlns="urn:schemas-upnp-org:device-1-0">
<URLBase>base URL for all relative URLs</URLBase>
<device>
<friendlyName>short user-friendly title</friendlyName>
<manufacturer>manufacturer name</manufacturer>
<manufacturerURL>URL to manufacturer site</manufacturerURL>
<modelDescription>long user-friendly title</modelDescription>
<modelName>model name</modelName>
<modelNumber>model number</modelNumber>
<modelURL>URL to model site</modelURL>
<serialNumber>manufacturer's serial number</serialNumber>
<UDN>uuid:UUID</UDN>
<UPC>Universal Product Code</UPC>
<deviceType>urn:schemas-upnp-org:device:deviceType :v</deviceType>
<serviceList>
<service>
<serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType>
<serviceId>urn:upnp-org:serviceId:serviceID</serviceId>
<SCPDURL>URL to service description</SCPDURL>
<controlURL>URL for control</controlURL>
<eventSubURL>URL for eventing</eventSubURL>
</service>
Declarations for other services (if any) go here
</serviceList>
<deviceList>Description of embedded devices (if any) go here</deviceList>
<iconList>
<icon>
<mimetype>image/format</mimetype>
<width>horizontal pixels</width>
<height>vertical pixels</height>
<depth>color depth</depth>
<url>URL to icon</url>
</icon>
XML to declare other icons, if any, go here
</iconList>
<presentationURL>URL for presentation</presentationURL>
</device>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
Page
<?xml version="1.0"?>
<root xmlns="urn:schemas-upnp-org:device-1-0">
<URLBase>base URL for all relative URLs</URLBase>
<device>
<friendlyName>short user-friendly title</friendlyName>
<manufacturer>manufacturer name</manufacturer>
<manufacturerURL>URL to manufacturer site</manufacturerURL>
<modelDescription>long user-friendly title</modelDescription>
<modelName>model name</modelName>
<modelNumber>model number</modelNumber>
<modelURL>URL to model site</modelURL>
<serialNumber>manufacturer's serial number</serialNumber>
<UDN>uuid:UUID</UDN>
<UPC>Universal Product Code</UPC>
<deviceType>urn:schemas-upnp-org:device:deviceType :v</deviceType>
<serviceList>
<service>
<serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType>
<serviceId>urn:upnp-org:serviceId:serviceID</serviceId>
<SCPDURL>URL to service description</SCPDURL>
<controlURL>URL for control</controlURL>
<eventSubURL>URL for eventing</eventSubURL>
</service>
Declarations for other services (if any) go here
</serviceList>
<deviceList>Description of embedded devices (if any) go here</deviceList>
<iconList>
<icon>
<mimetype>image/format</mimetype>
<width>horizontal pixels</width>
<height>vertical pixels</height>
<depth>color depth</depth>
<url>URL to icon</url>
</icon>
XML to declare other icons, if any, go here
</iconList>
<presentationURL>URL for presentation</presentationURL>
</device>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</root>
</root>
9

## Slide 10: Device Description – display information
0
Page 1
<?xml version="1.0"?>
<root xmlns="urn:schemas-upnp-org:device-1-0">
<URLBase>base URL for all relative URLs</URLBase>
<device>
<friendlyName>short user-friendly title</friendlyName>
<manufacturer>manufacturer name</manufacturer>
<manufacturerURL>URL to manufacturer site</manufacturerURL>
<modelDescription>long user-friendly title</modelDescription>
<modelName>model name</modelName>
<modelNumber>model number</modelNumber>
<modelURL>URL to model site</modelURL>
<serialNumber>manufacturer's serial number</serialNumber>
<UDN>uuid:UUID</UDN>
<UPC>Universal Product Code</UPC>
<deviceType>urn:schemas-upnp-org:device:deviceType</deviceType>
<serviceList>
<service>
<serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType>
<serviceId>urn:upnp-org:serviceId:serviceID</serviceId>
<SCPDURL>URL to service description</SCPDURL>
<controlURL>URL for control</controlURL>
<eventSubURL>URL for eventing</eventSubURL>
</service>
Declarations for other services (if any) go here
</serviceList>
<deviceList>Description of embedded devices (if any) go here</deviceList>
<iconList>
<icon>
<mimetype>image/format</mimetype>
<width>horizontal pixels</width>
<height>vertical pixels</height>
<depth>color depth</depth>
<url>URL to icon</url>
</icon>
XML to declare other icons, if any, go here
</iconList>
<presentationURL>URL for presentation</presentationURL>
</device>
<specVersion>
<major>1</major> <minor>0</minor>
</specVersion>
</root>
<?xml version="1.0"?>
<root xmlns="urn:schemas-upnp-org:device-1-0">
<URLBase>base URL for all relative URLs</URLBase>
<device>
<friendlyName>short user-friendly title</friendlyName>
<manufacturer>manufacturer name</manufacturer>
<manufacturerURL>URL to manufacturer site</manufacturerURL>
<modelDescription>long user-friendly title</modelDescription>
<modelName>model name</modelName>
<modelNumber>model number</modelNumber>
<modelURL>URL to model site</modelURL>
<serialNumber>manufacturer's serial number</serialNumber>
<UDN>uuid:UUID</UDN>
<UPC>Universal Product Code</UPC>
<deviceType>urn:schemas-upnp-org:device:deviceType</deviceType>
<serviceList>
<service>
<serviceType>urn:schemas-upnp-org:service:serviceType:v</serviceType>
<serviceId>urn:upnp-org:serviceId:serviceID</serviceId>
<SCPDURL>URL to service description</SCPDURL>
<controlURL>URL for control</controlURL>
<eventSubURL>URL for eventing</eventSubURL>
</service>
Declarations for other services (if any) go here
</serviceList>
<deviceList>Description of embedded devices (if any) go here</deviceList>
<iconList>
<icon>
<mimetype>image/format</mimetype>
<width>horizontal pixels</width>
<height>vertical pixels</height>
<depth>color depth</depth>
<url>URL to icon</url>
</icon>
XML to declare other icons, if any, go here
</iconList>
<presentationURL>URL for presentation</presentationURL>
</device>
<specVersion>
<major>1</major> <minor>0</minor>
</specVersion>
</root>

## Slide 11: Services
Page 11
Logical grouping of functions and (state) variable definition
Examples:
Connection Manager service: A set of functions that are used to negotiate which protocol to use for communication
Content Directory service: set of functions that describe the content available on a server
Rendering Control (service): set of functions that change settings like volume, brightness, contrast etc.
Media Renderer: set of functions to control playback (via the network)
State variables are used 2 two ways
  Conveying state, like SystemUpdateID of the CDS
  Type definition of arguments in actions
    preceded by A_ARG_TYPE_

## Slide 12: Service Description ‐ actions
2
Page 1
<?xml version="1.0"?>
<scpd xmlns="urn:schemas-upnp-org:service-1-0">
<actionList>
<action>
<name>actionName</name>
<argumentList>
<argument>
<name>formalParameterName</name>
<direction>in xor out</direction>
<retval />
<relatedStateVariable>stateVariableName</relatedStateVariable>
</argument>
Declarations for other arguments (if any) go here
</argumentList>
</action>
Declarations for other actions (if any) go here
</actionList>
<serviceStateTable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable datatype</dataType>
<defaultValue>default value</defaultValue>
<allowedValueRange>
<minimum>minimum value</minimum>
<maximum>maximum value</maximum>
<step>increment value</step>
</allowedValueRange>
</stateVariable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable data type</dataType>
<defaultValue>default value</defaultValue>
<allowedValueList>
<allowedValue>some value</allowedValue>
<allowedValue>some value</allowedValue>
</allowedValueList>
</stateVariable>
Declarations for other state variables (if any) go here
</serviceStateTable>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</scpd>
<?xml version="1.0"?>
<scpd xmlns="urn:schemas-upnp-org:service-1-0">
<actionList>
<action>
<name>actionName</name>
<argumentList>
<argument>
<name>formalParameterName</name>
<direction>in xor out</direction>
<retval />
<relatedStateVariable>stateVariableName</relatedStateVariable>
</argument>
Declarations for other arguments (if any) go here
</argumentList>
</action>
Declarations for other actions (if any) go here
</actionList>
<serviceStateTable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable datatype</dataType>
<defaultValue>default value</defaultValue>
<allowedValueRange>
<minimum>minimum value</minimum>
<maximum>maximum value</maximum>
<step>increment value</step>
</allowedValueRange>
</stateVariable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable data type</dataType>
<defaultValue>default value</defaultValue>
<allowedValueList>
<allowedValue>some value</allowedValue>
<allowedValue>some value</allowedValue>
</allowedValueList>
</stateVariable>
Declarations for other state variables (if any) go here
</serviceStateTable>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</scpd>

## Slide 13: Service Description – state variables
<?xml version="1.0"?>
<scpd xmlns="urn:schemas-upnp-org:service-1-0">
<actionList>
<action>
<name>actionName</name>
<argumentList>
<argument>
<name>formalParameterName</name>
<direction>in xor out</direction>
<retval />
<relatedStateVariable>stateVariableName</relatedStateVariable>
</argument>
Declarations for other arguments (if any) go here
</argumentList>
</action>
Declarations for other actions (if any) go here
</actionList>
<serviceStateTable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable datatype</dataType>
<defaultValue>default value</defaultValue>
<allowedValueRange>
<minimum>minimum value</minimum>
<maximum>maximum value</maximum>
<step>increment value</step>
</allowedValueRange>
</stateVariable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable data type</dataType>
<defaultValue>default value</defaultValue>
<allowedValueList>
<allowedValue>some value</allowedValue>
<allowedValue>some value</allowedValue>
</allowedValueList>
</stateVariable>
Declarations for other state variables (if any) go here
</serviceStateTable>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</scpd>
<?xml version="1.0"?>
<scpd xmlns="urn:schemas-upnp-org:service-1-0">
<actionList>
<action>
<name>actionName</name>
<argumentList>
<argument>
<name>formalParameterName</name>
<direction>in xor out</direction>
<retval />
<relatedStateVariable>stateVariableName</relatedStateVariable>
</argument>
Declarations for other arguments (if any) go here
</argumentList>
</action>
Declarations for other actions (if any) go here
</actionList>
<serviceStateTable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable datatype</dataType>
<defaultValue>default value</defaultValue>
<allowedValueRange>
<minimum>minimum value</minimum>
<maximum>maximum value</maximum>
<step>increment value</step>
</allowedValueRange>
</stateVariable>
<stateVariable sendEvents=“yes” xor “no”>
<name>variableName</name>
<dataType>variable data type</dataType>
<defaultValue>default value</defaultValue>
<allowedValueList>
<allowedValue>some value</allowedValue>
<allowedValue>some value</allowedValue>
</allowedValueList>
</stateVariable>
Declarations for other state variables (if any) go here
</serviceStateTable>
<specVersion>
<major>1</major><minor>0</minor>
</specVersion>
</scpd>

## Slide 14: UPnP Phases (Control)
3 Send actions to a device using SOAP Receive responses using SOAP
Remote procedure call mechanism based on SOAP.
2 Description
1 Discovery
0 Addressing
5 Protocol
4 Eventing
3 Control

## Slide 15: Remote Procedure Calls
POST path of control URL HTTP/1.1
HOST: host of control URL:port of control URL
CONTENT-TYPE: text/xml; charset="utf-8"
SOAPACTION: "urn:schemas-upnp-org:service:serviceType:v#actionName"
Based on SOAP (IETF Draft Simple Object Access Protocol)
= XML messages using HTTP headers
POST path of control URL HTTP/1.1
HOST: host of control URL:port of control URL
CONTENT-TYPE: text/xml; charset="utf-8"
SOAPACTION: "urn:schemas-upnp-org:service:serviceType:v#actionName"
<s:Envelope xmlns:s="http://schemas.xmlsoap.org/soap/envelope/" s:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
<s:Body>
<u:actionName xmlns:u="urn:schemas-upnp-org:service:serviceType:v">
<argumentName>in arg value</argumentName> other in args and their values (if any) go here
</u:actionName>
</s:Body>
</s:Envelope>

## Slide 16: Remote Procedure Call Response
Response by device:
HTTP/1.1 200 OK
CONTENT-TYPE: text/xml; charset="utf-8"
<s:Envelope xmlns:s="http://schemas.xmlsoap.org/soap/envelope/" s:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
<s:Body>
</s:Body>
</s:Envelope>
HTTP/1.1 200 OK
CONTENT-TYPE: text/xml; charset="utf-8"
<s:Envelope xmlns:s="http://schemas.xmlsoap.org/soap/envelope/" s:encodingStyle="http://schemas.xmlsoap.org/soap/encoding/">
<s:Body>
<u:actionNameResponse
xmlns:u="urn:schemas-upnp-org:service:serviceType:v">
<argumentName>out arg value</argumentName> other out args and their values (if any) go here
</u:actionNameResponse>
</s:Body>
</s:Envelope>
It’s always 200 ok, even if it has an error

## Slide 17: UPnP Phases (Eventing)
4
Control points can subscribe to events from a certain device
Events are send by device to control point when a state variable changes.
E.g. ContainerUpdateID, Volume (LastChange)
GENA ‐ IETF Draft General Event Notification Architecture Message over HTTP via TCP, but also via UDP multicast
2 Description
1 Discovery
0 Addressing
5 Protocol
4 Eventing
3 Control

## Slide 18
GENA stands for General Event Notification Architecture.
GENA Base defines an HTTP notification architecture that transmits notifications between HTTP resources. An HTTP resource could be any object which might need to send or receive a notification, for example a distribution list, buddy list, print job, etc. It was defined in Internet-Draft draft-cohen-gena-p-base-01.txt (now expired).
Alexandre VERDET:Con : it is not very energy effective
girard:it is insecure
Jehad Melad:using SOAP maybe can be a disadvantage
Cédric Gormond:Pro : Upnp is a great architecture for home devices and networks.
dhayananth:SOAP based would be disadvantages. because we implementation would be difficult. also XML is less convenient

## Slide 19: GENA ‐ Subscribe
Control points subscribe per Service and Device.
Control point is in control for which service it will receive the notifications
All notifications per service will be received.
Have to re‐subscribe before TIMEOUT elapses
SUBSCRIBE publisher path HTTP/1.1
HOST: publisher host:publisher port
SUBSCRIBE publisher path HTTP/1.1 HOST: publisher host:publisher port CALLBACK: <delivery URL>
NT: upnp:event
TIMEOUT: Second-requested subscription duration

## Slide 20: GENA ‐ Notify
Device sends same property set to each subscribed control point
Sequence (SEQ) is tracking initial & following notification
Initial notification is ALWAYS sent by the device
NOTIFY delivery path HTTP/1.1
HOST: delivery host:delivery port
CONTENT-TYPE: text/xml
NOTIFY delivery path HTTP/1.1 HOST: delivery host:delivery port CONTENT-TYPE: text/xml
NT: upnp:event
NTS: upnp:propchange SID: uuid:subscription-UUID SEQ: event key
<e:propertyset xmlns:e="urn:schemas-upnp-org:event-1-0">
<e:property>
<variableName>new value</variableName>
</e:property>
Other variable names and values (if any) go here
</e:propertyset>

## Slide 21: UPnP Phases (Protocol)
2 Description
1 Discovery
0 Addressing
5 List of logical sequences on top of Control and Eventing.
Control point interacts with multiple devices to create an scenario.
Also control points should listen to events, so they know what has changed in the eco system, and should reflect this in their UI.
5 Protocol
4 Eventing
3 Control

## Slide 22: Protocol example (sequence of actions)
Steps needed to play an item from a Media Server on a Media Renderer
Select a Media server
Invoke Browse(), to present content for selection for playback
Select a Media Server
Invoke GetProtocolInfo() on the Media Renderer
Match the ProtocolInfo from the content and the MediaRenderer
Invoke SetAVTransportURI() with the matched content
Invoke Play(), to start the playback of the content

## Slide 23
For the interconnected lifestyle