## Slide 1
EnOcean technology for intelligent and green buildings.
Author

## Slide 2: Overview
Page 2
Why wireless & batteryless?
EnOcean – the batteryless wireless technology
Installation
Radio: Basics & range planning
Support & next steps

## Slide 3: Current state with many installations
Page 3

## Slide 4: Current state
Page 4

## Slide 5: Current state
Page 5
These are not really SmartPlugs falling under the IOT category. But the effort to make something like this, and the result was close to Smart Plugs.
More details on Smart Plugs need to be found out

## Slide 6: Current state
Page 6
To control a lot of different equipments, Eg: two remotes for controlling the tv, but 1 is specifically used for tv switchOnOff and other for the set-top box

## Slide 7: Cable: expensive & inflexible
Conventional wiring solutions
Time consuming
Material-intensive
Building Mess & Noise
Inflexible: This term is used, because this inserting wires in to the building walls need to be done before hand. And in case, you need to change the wiring then probably, you can still use the smallPathsInstalledForTheWires but the wiring system would need upgrade. Recall previous
Expensive Over Building Lifespan
High costs with retrofitting(add (a component or accessory) to something that did not have it when manufactured.) and change of use
Page 7

## Slide 8: Conventional wireless technology requires batteries
Page 8
Batteries require:
Monitoring & Tracking for the battery level
Stocking
Access and replacement
Costly Disposal for planet.
Batteries :
Cause Pollution
Require regular replacement

## Slide 9: Customer wishes and modern house technology requirements
Easy use and install
Suitable for simple and complex applications
Simple function changes possible
Upgradeable, expandable and flexible at any time
Adaptable to technical innovations
Wide range of products and manufacturers
Good price/performance ratio
Page 9

## Slide 10: The solution: EnOcean standard
Page 10
Batteryless , wireless standard from EnOcean for intelligent buildings
High degree of flexibility
Comfort & security
Cost-saving
Reliable, future-proof technology
Energy efficiency
Low/No Maintenance
No wiring required for sensors
Involving no battery here in regards to sensors and actuators would mean that they would be capable
to generate their own energy

## Slide 11: EnOcean – your chance in the installer market
Shift to system business
Better distinction from the competition (unique characteristics)
Easy entry in EnOcean technology possible
Additional business (scalable offering - from small installations to automation)
Ready for law reforms, e.g. the EnEV 2014 in Germany
Page 11

## Slide 12: Overview
Page 12
Why wireless & batteryless?
EnOcean – the batteryless wireless technology
Installation
Radio: Basics & range planning
Support & next steps

## Slide 13
EnOcean – the radio standard for green buildings
No Wires
  more than 1,200 interoperable products
  International radio standard (ISO/IEC)
  ISO/IEC JTC 1
No Batteries
  Maintenance free
  Environmentally friendly
No Limits
  Maximum flexibility
  More than 250,000 equipped buildings
Page 13

## Slide 14
Enocean’s popularity is very low

## Slide 15: Batteryless wireless technology for residential markets/ smart homes
© EnOcean Alliance | Intelligent and Green Buidlings | 2014
Page 14

## Slide 16: EnOcean – the basis for smart homes and building automation
© EnOcean Alliance | Intelligent and Green Buidlings | 2014
Page 15

## Slide 17: Batteryless wireless technology for building automation
© EnOcean Alliance | Intelligent and Green Buidlings | 2014 Page
© EnOcean Alliance | Intelligente Gebäude | Aug 2013
16
16

## Slide 18
Batteryless wireless technology from EnOcean
= energy harvester + radio modules
https://www.enocean.com/en/products/

## Slide 19: Energy Harvesting
Kinetic energy
Electrodynamic generator
Solar energy
Module with energy storage
Thermal energy
Energy generation through temperature differences

## Slide 20: Basics of EnOcean radio
EnOcean radio
Energy generation through press of a button, light, differences in temperature
Wireless protocol: EnOcean ISO/IEC-Standard 14543-3-10
Frequency: license-free frequency band under 1 GHz (868 MHz in Europe and China, 902 MHz in North America, 928 MHz in Japan)
uni/bidirectional communication
Range
About 30m in buildings
Range extension with repeaters (Level 1 and Level 2)
Transmission security
short telegrams ~ 1ms
2 asynchronous repetitions
Encryption and Rolling Code (authentication)
Interoperability
each transmitter has an unique address (32Bit-ID)
standardized protocol and sensor profiles (EEP)
EnOcean Equipment Profiles (EEP's)

## Slide 21: EnOcean is more environmentally friendly – than any other wireless devices
COMPARISON OF HIGH FREQUENCY DEVICES
Device/ System W/m² Distance (m) Duration
EnOcean wireless switch 0,000013 1
few ms during actuation
Convent. light switch
0,0015
1
few ms during actuation
WiFi Access Point
0,01
2
during data exchange
Network card
0,1
0,5
during data exchange
DECT telephone
1
during phone call
Cell phone
12-42
during phone call
Cellular base station
0,00001 - 0,1
diverse permanence
100 x
700 x
7.000 x
70.000 x
0,1
1,6 Mio.x av0e,1rage
The "watt per square meter" is the SI unit for radiative and other energy fluxes in geophysics. The "solar constant", the solar irradiance at the mean earth-sun distance is approximately 1370 W m-2.

## Slide 22: EnOcean-based products – www.enocean-alliance.org/products

## Slide 23: Multi-vendor interoperable solution for residential buildings/ smart homes
Central Units
Switches and Sensors Actuators
Merten Gira, Berker Jung
Easyfit
LAN/WLAN

## Slide 24: Multi-vendor interoperable solutions for building automatoin
Building automation
Switches and Sensors Actuators
Merten Gira, Berker Jung
Easyfit
LAN/WLAN

## Slide 25: Further applications with EnOcean
Pressure sensors for furniture and mattresses
Handheld transmitters for door operators
Mousetraps
Bus stop buttons
Industrial switches
Cable harness sensors
Avalanche protection sensors
….
24

## Slide 26: References for residential buildings/ smart homes
EnOcean is worthwhile, from the first Switch-Receiver-Combination in:
Apartments
Detached and semi-detached homes
Prefabricated houses
Small commercial properties (e.g. practices, offices)

## Slide 27: Over 250.000 buildings worldwide –“enabled by EnOcean"
Industrial buildings
Offices
Residential buildings
Hospitals
Hotels
Historical buildings
Schools/ Universities
Stores

## Slide 28: Activities of the EnOcean Alliance
Basis is the wireless standard for self- powered wireless applications
  ISO/IEC Standard 14543-3-10
  Application profiles EnOcean Equipment Profiles (EEP)
Secures interoperability of Endproducts
More than 350 members
  Product manufacturers
  System integrators
  Specifiers, architects
  Installers
Worldwide activities and networks

## Slide 29: Benefits for installers and specifiers
Easy installation
Easy planning and highest flexibility through freely positionable sensors
Less noise and dirt
Upgradeable and extendable at any time
Wide range of interoperable products from various manufacturers
Reliable and future-proof technology

## Slide 30: Overview
Why wireless & batteryless?
EnOcean – the batteryless wireless technology
Installation
Radio: Basics & range planning
Support & next steps

## Slide 31: Easy installation: 1x Switch and 1x Receiver
Step 1:
  Connect electrical loads with actuators (luminaires, shutters, sockets, heating valves).

Step 2:
  Link switches and sensors once using the easy teach-in mode in the actuator.
One base installation = many functions

## Slide 32
An actuator is a device that uses a form of power to convert a control signal into mechanical motion. From electric door locks in automobiles, to ailerons on aircraft, actuators are all around us.
Philips Hue is a line of color changing LED lamps and white bulbs which can be controlled wirelessly. The Phillips Hue line of bulbs was the first smart bulb of its kind on the market.

## Slide 33: Easy installation: optional extension
Step 3 (optional)
  Visualization with Touch-Panel
  Connecting video cameras
  Connection to the internet (Smart phone/PDA/Tablet)

## Slide 34: Advantages for your clients
More comfort
  Central functions
  Scenes
  Automation
  Visualization/Touch-Panel
More security
  Window monitoring
  Panic button
  Presence simulation
More energy efficiency
  Heating control combined with window monitoring
  Individual zone regulation/individual room control
…with user-friendy technology!

## Slide 35: Advantages for the user: flexibility
Changes in the house – position switches in any location
In case of changes in furnishing
  New furniture
  New room layout
Conversion
  Office room
  Nursery
  Nursing care
Simple retrofit
  Handheld switch
  Additional switches
  Connection to exterior lighting
  Pump in the garden pond

## Slide 36: Freely positionable switches
Nursery – the switch is glued directly next to the bed – it’s safe as well as there is no direct electrical connection

## Slide 37: Freely positionable switches – furniture
Bedroom – switch next to the bed

## Slide 38: Freely positionable switches – glass
Bathroom – the switch can be next to the bath or shower

## Slide 39: Remote control – scenes
Control blinds, dim lights, open doors
37

## Slide 40: Remote control – garage door

## Slide 41: More comfort with remote control
Control Lighting
  Central on/off
  Scenes
Control Blinds
  Single/groups
  Central on/off
Control Multimedia
Heating Control

## Slide 42: Decentralized control – Blinds
Ideal for retrofits
  No cables
  Switches freely positionable
Functions
  Individual control
  Group control
  Central control
  Automation
  Dimming
  Light scenes
Components

## Slide 43: Decentralized control – Lighting
Components
Switching actuators
Switches

## Slide 44: Central control – easily expandable
Functions
  Individual control
  Group control
  Central control
  Automation
  Dimming
  Light scenes
Garden illumination
Garden pump

## Slide 45: Individual heating control
Functions
  Timer
  Heating times programmable
  Remote access possible
Components
Thermostats
Switching actuators for heating valves

## Slide 46: Residential house in Schorndorf
Modern residential house
Problem
  Running cables difficult – exposed concrete
Solution
  EnOcean-based switches and thermostat
Advantages
  Flexibility
  Easy installation
  Lower costs

## Slide 47: Prefabricated houses with EnOcean technology
50% of all WeberHaus buildings are equipped with EnOcean technology
45

## Slide 48: Commercial buildings: connection to b us systems
Building automation
Switches and sensors Actuators
Merten Gira, Berker Jung
Easyfit
LAN/WLAN
© EnOcean Alliance | Intelligent and Green Buidlings | 2014
46
Page 46
© EnOcean Alliance | Intelligente Gebäude | Aug 2013

## Slide 49: Commercial buildings: axis-orientated installation with room controller
Fassade
Fassade
Receiver, radius ca. 15m
1 Room controller for 8 building axis
Building axis
Receiver
BUS supply Mains supply
Floor

## Slide 50: Functional buildings: flexible room structures with wireless technology
Front
Floor
Building axis
EnOcean Wireless Standard = Maximum Flexibility

## Slide 51: Commerical buildings: advantages for the user
High energy efficiency due to optimal building automation
Simple planning - Easy adjustment if changes occur during the building phase
Highly flexible office areas
Lower running costs with changes in room structure or after a change in tenants
49

## Slide 52: Commercial buildings: Advantages for installers and planners
Easy planning and highest flexibility through freely positionable sensors
Less noise and dirt
Flexible room layout
Upgradeable and expandable at any time
Wide range of interoperable products and manufacturers
Compatibility with other building automation systems (e.g. EIB/KNX, LON, BACnet und TCP/IP)

## Slide 53: Commercial buildings: The Squaire (AirRail Center)
The Squaire – Frankfurt, Germany
  12.000 batteryless wireless modules from EnOcean

## Slide 54: Over 250.000 buildings worldwide – „enabled by EnOcean"
Industrial buildings
Offices
Residential buildings
Hospitals
Hotels
Historical buildings
Schools/ Universities
Stores

## Slide 55: Overview
Why wireless & batteryless?
EnOcean – the batteryless wireless technology
Installation
Radio: Basics & planning
Support & next steps

## Slide 56: Basics of radio signals
Range of wireless signals
  Wireless signals are electromagnetic waves – the field strength at the receiver decreases as the distance to the emitter increases
  In order to achieve maximum range, visual contact is not sufficient
  A free zone (Fresnel zone) is required between transmitter and receiver; this zone is an ellipse
  No interference from other wireless frequencies and radio applications such as Wi- Fi, garage doors, weather stations

## Slide 57: Basics of radio signals in praxis
Typical range in practice
In a building with ideal conditions
  30m, large open space
It’s best practice to plan max. 15m (planning security)
  Possible losses due to furniture, persons, subsequent walls

## Slide 58: Basics of radio signals
Radio transmission occurs as an ellipse
For maximum range,’ line of site ‘is not sufficient
At a 30m range, the ellipse centre is theoretically around 10m. Narrow corridors with massive walls are therefore unfavorable.
Transmitter Tx
Receiver Rx

## Slide 59: Basics of radio signals – absorption
Absorption
  Radio can penetrate walls – but signals are absorbed
  Absorption rate depends on material
Examples
  Wood, plaster, uncoated glass, no metal 0 – 10%
  Bricks, press boards 5 – 35%
  Concrete with iron reinforcement 10 – 90%
  Metal, aluminium lining 90 – 100%

## Slide 60: Basics of radio signals – penetration angle
Depending on the angle, the effective wall strength and absorption of the signal changes
Whenever possible, the signals should go vertically through the walls. Niches in walls are to be avoided
If flat penetration angles occur, repositioning of transmitter and/or receiver antennas or the use of a repeater is recommended

## Slide 61: Basics of radio signals – antenna installation & sources of interference
Radio coverage along a wall area is to be avoided (e.g. also in a long corridor)
Whilst laying out a shielded antenna cable, take note not to bend the cable, to do so could damage it beyond repair
The distance from the EnOcean receiver to other high frequency transmitters should be a of min. 50 cm, the position isn’t critical. 868 MHz-RFID shouldn’t be used in the same room

## Slide 62: Optimal positioning of solar-based sensors
Ambient light > 50 lux:
powers sensor and charges super capacitor
3 hours with 200 lux: enough energy for 14 hours in darkness
Fully charged devices can function
3 -5 days in darkness

## Slide 63: Required amount of light in buildings
School
  Blackboard
  Typical schoolroom
500 – 1000 lx
300 – 500 lx
Office building
  PC-work place
  Conference room
  Corridor
200 – 500 lx
300 – 700 lx
50 – 100 lx
Hotel
  Reception
  Restaurant
  Staircase
300 – 700 lx
150 – 300 lx
50 – 150 lx

## Slide 64: Range planning : tools
EPM 300 to check the possible range in buildings or outside
Level 1- and Level 2-repeater
System optimization possibilities: transmitters are received by 2 gateways
Information brochure „Range Planning Guide” to download:
http://www.enocean.com/fileadmin/redaktion/pdf/ app_notes/AN001_RANGE_PLANNING_2013_ en.pdf

## Slide 65: Range planning for residential buildings
Repeater not normally needed
Normal wall strength
No aluminum / foil lining in walls
10m
10m
Transmitter or Receiver

## Slide 66: Range planning for residential buildings
Repeater are recommended
  At central point
  Many actuators already have integrated repeater functions
Transmitter Or Receiver

## Slide 67: Range planning in commercial buildings: Step 1
Take a Building Floor Plan and a Drawing Circle
Mark relevant Radio Shadings into the Floor Plan
  Fire Protection Walls
  Lavatories, Staircases, Elevator Shafts, Supply Areas….

## Slide 68: Range planning in commercial buildings: Step 2
Draw in the receiving radii 10m–15m
10m-radii guarantee enough planning reserves Circle center = receiver position (+/- 1m is ok )
= 20m

## Slide 69: Range planning in functional buildings: Connectivity to automation systems
Gateways can also be added to existing building automation systems.
Approach:
  Which central building control system is used?
  Which applications are desired?
  Which products are to be used?
  How many emitters per unit (axis, area, etc.) are desired?

## Slide 70: Overview
Why wireless & batteryless?
EnOcean – the batteryless wireless technology
Installation
Radio: Basics & planning
Support & next steps

## Slide 71: Start now with EnOcean!
Simple entry: retrofit with a decentralized solution
  e.g. a switch and an actuator
  Search for a fitting solution from over 1.200 interoperable products
More information and training can be found directly at the OEMs
http://www.enocean-alliance.org/en/wheretobuy/

## Slide 72
Products –
http://www.enocean-alliance.org/en/products/
© EnOcean Alliance | Intelligent and Green Buidlings | 2014 Page 70

## Slide 73: Find your solution – http://www.enocean-alliance.org/en/solutionfinder/
71
Page 73

## Slide 74
Available here –
http://www.enocean-alliance.org/en/wheretobuy/
Page 74

## Slide 75
References –
http://www.enocean-alliance.org/en/references/
Page 75

## Slide 76: Useful information
Page 76
Coverage planning: http://www.enocean.com/fileadmin/redaktion/pdf/app_notes/AN001_RANGE_PL ANNING_2013_en.pdf
Brochures:
http://www.enocean-alliance.org/en/downloads/
Technical information:
http://www.enocean-alliance.org/en/white_papers/
Videos: www.youtube.com/user/EnOcean
Social Media
  Twitter: http://twitter.com/enoceanalliance
  Facebook: www.facebook.com/pages/EnOcean-Alliance/109269292485427
  LinkedIn: http://www.linkedin.com/groups?mostPopular=&gid=3578554
  Google+: https://plus.google.com/u/0/107585984916165196922

## Slide 77
EnOcean Alliance
2400 Camino Ramon, Suite 375 San Ramon, CA 94583
USA
Phone US: +1.925.275-6601
info@enocean-alliance.org www.enocean-alliance.org
Page 77